## Slide 1: Kathará
A container-based framework for experimenting computer networking
Version | 2.1
Author(s) | L. Ariemma, G. Bonofiglio, G. Di Battista, V. Iovinella, G. Lospoto, M. Patrignani, M. Pizzonia, M. Rimondini
E-mail | contact@kathara.org
Web | https://www.kathara.org/
Description | An introduction to the architecture, setup and usage of Kathará – based on a similar presentation of Netkit

## Slide 2: Copyright notice
All the pages/slides in this presentation, including but not limited to, images, photos, animations, videos, sounds, music, and text (hereby referred to as “material”) are protected by copyright.
This material, with the exception of some multimedia elements licensed by other organizations, is property of the authors and/or organizations appearing in the first slide.
This material, or its parts, can be reproduced and used for didactical purposes within universities and schools, provided that this happens for non-profit purposes.
Information contained in this material cannot be used within network design projects or other products of any kind.
Any other use is prohibited, unless explicitly authorized by the authors on the basis of an explicit agreement.
The authors assume no responsibility about this material and provide this material “as is”, with no implicit or explicit warranty about the correctness and completeness of its contents, which may be subject to changes.
This copyright notice must always be redistributed together with the material, or its portions.

## Slide 3: About computer networks
Computer networks are quite complex
  Several devices (computers, routers, etc.)
  Several interfaces
  Several protocols running
  Physical interconnections originate complex topologies

## Slide 4: Example of a computer network
router-A
0:3
.1
0:4
.2
router-B
0:6
.1
0:8
.2
router-C
10.10.20.0/30
10.10.10.0/30
100.0.2.0/24
.55
.1
C:55
0:7
W1
100.0.3.0/24
.1
.77
0:5
C:77
D2
100.0.0.0/24
.33
.1
C:33
0:1
D1
100.0.1.0/24
.1
.22
0:2
C:22
W2
.11
C:11
P1
P2
A:2
.44
Internet

## Slide 5: How to perform experiments?
Performing experiments may be unfeasible
A live network cannot be exploited for experiments
  It hosts services that are critical for the company
  It would be necessary to coordinate different departments of the company
Network equipment is expensive
  Sometimes, even for performing simple experiments, several equipment should be available in the same test bed

## Slide 6: Simulation vs. emulation
Emulation and simulation systems put at user’s disposal a virtual environment that can be exploited for tests, experiments, measures
Simulation systems aim at reproducing the performance of a real-life system (latency time, packet loss, etc.)
  e.g.: ns, real, …
Emulation systems aim at accurately reproducing the functionalities of a real-life system (configurations, architectures, protocols), with limited attention to performance

## Slide 7: Kathará
a system for emulating computer networks

## Slide 8: Emulating a network
Basic idea:
  several containers are created inside a single host machine
  containers are connected to virtual collision domains and thus can communicate with each other
Each container can be configured as a device that plays the role of a regular host, of a router, of a switch, ….

## Slide 9: Docker and containers
A container is a standard unit of software that packages up code and all its dependencies, so the application runs quickly and reliably from one computing environment to another.
https://www.docker.com/resources/what-container

## Slide 10: Kathará
Based on Docker
Each emulated network device (in what follows device) is a container
Note: several container images available, e.g.:
  Base (DNS, Web Server, network utilities)
  Quagga (standard routing protocols)
  FRRouting (standard routing protocols + EVPN + MPLS)
  Open vSwitch (Open Flow enabled switch)
  Behavioral Model (software implementation of a P4 switch)

## Slide 11: Emulated network devices
Each device has:
  A console (a terminal window)
  A memory
  A filesystem
  (zero, one or more) network interfaces
Each network interface is connected to a single (virtual) collision domain
Each virtual collision domain can be connected to several interfaces

## Slide 12
user@host$ █
host machine
host machine
console
pc3
collision
domain A
pc1
pc2
collision
domain B
root@pc1:~$ █
root@pc3:~$ █
root@pc2:~$ █

## Slide 13: Setting up Kathará
Setup manual

## Slide 14: Installing Kathará
Available for:
  Windows
  Linux
  MacOS
Download at https://www.kathara.org/
Follow the wiki

## Slide 15: Changing the default Docker Image
Run kathara settings
Select Choose default image by pressing 2
Select kathara/frr by pressing 2
Confirm and exit

## Slide 16: Using Kathará

## Slide 17: Kathará commands
Kathará provides users with three sets of commands
  v-prefixed commands (v-commands)
  l-prefixed commands (l-commands)
  Global commands
v-commands act as low-level tools for configuring and starting up a single device
l-commands provide an easier-to-use environment to set up complex labs consisting of several devices
Global commands are mainly management commands

## Slide 18: Kathará v-commands
Allow to startup a single device with arbitrary configurations (network interfaces, etc.)
  vstart: starts a new device
  vconfig: attaches network interfaces to a running device
  vclean: halts a device

## Slide 19: Kathará l-commands
Ease setting up complex labs consisting of several virtual machines
  lstart: starts a Kathará lab
  lclean: halts all the devices of a lab
  lrestart: halts all the devices of a lab and start them again
  linfo: provides information about a lab

## Slide 20: Kathará global commands
Management commands
  check: Check your system environment
  connect: Connect to a running Kathará machine
  list: Show all running Kathará machines of the current user
  settings: Show and edit Kathará settings
  wipe: Delete all Kathará machines and links, optionally also delete settings

## Slide 21: Testing Kathará

## Slide 22: Testing Kathará
To test if your setup works correctly run:
  kathara check
    This command will ran automatic tests to your environment
  kathara vstart -n pc1 --eth 0:A
    This command will start a new device called pc1 and connected to the virtual collision domain A
    A terminal window will open allowing to run commands inside the device
  kathara vclean -n pc1
    This command will stop the previous started device

## Slide 23: Preparing a Kathará lab

## Slide 24: Kathará lab
a Kathará lab is a set of preconfigured devices that can be started and halted together
a basic Kathará lab is a directory tree containing:
  a lab.conf file describing the network topology
  a set of subdirectories that contain the configuration settings for each device
  <device_name>.startup files that describe actions performed by devices when they are started

## Slide 25: lab.conf
describes:
  The topology of the network that interconnects the lab’s devices
  The devices to be started
contain a list of machine[arg]=value lines where:
  machine is the name of the device (e.g. pc1)
  if arg is a number, then value is the name of a collision domain to which etharg should be attached
  if arg is not a number, then it must be an option and value the argument

## Slide 26: lab.conf
example
pc1[0]=A
pc2[0]=A
pc2[1]=B
pc3[0]=B
pc1
pc2
eth0
eth0
collision domain A
pc3
eth0
eth1
collision domain B

## Slide 27: Share files between the host and the devices
There are two ways to share files between the host filesystem and the device filesystem:
  Share files mirrored to the device
    A change inside the device will reflect in the host filesystem
    A change in the host filesystem will reflect in the device
  Share files copied to the device
    Two independent copies of the same files

## Slide 28: Share files mirrored to the device
There are two ways to share mirrored files:
  the /shared directory inside a device directly points to the shared directory inside the lab
    by default it is ENABLED, you can disable it in the settings
  the /hosthome directory inside a device directly points to the home directory of the current user of the host
    by default it is DISABLED, you can enable it in the settings

## Slide 29: Share files copied to the device
Can be done through the subdirectories of a lab
The contents of subdirectory device are copied into the root (/) of the device named device filesystem
  for example, pc1/foo/file.txt is copied to /foo/file.txt inside the device pc1

## Slide 30: .startup files
Shell scripts that are executed inside a device right after its startup
Typical usage of a .startup file is to configure network interfaces and/or start network services
  For example:
ifconfig eth0 10.0.0.1/24 up
/etc/init.d/frr start

## Slide 31: Launching/halting a lab
Open a terminal
Enter the lab directory (cd lab_directory)
Launch a Kathará l-command
  Where l-command could be one of the following
    kathara lstart, to start the lab
    kathara lclean, to stop the lab
    kathara lrestart, to restart the lab

## Slide 32: More information
Further information can be found:
  On GitHub’s Kathará wiki
  On the official website https://www.kathara.org
  Inside Kathará man pages
    On Linux and MacOS accessible by the terminal man kathara
    Available online at https://www.kathara.org/man-pages/kathara.1.html